## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID –
Problem Statement Title- NET COMPASS: Intelligent Cellular Network Coverage & Performance Monitoring System
Theme-
PS Category- Hardware
Team ID-
Team NET COMPASS — Dept. of Electronics & Communication Engineering

## Slide 2: IDEA TITLE
Proposed Solution (Describe your Idea/Solution/Prototype)
NET COMPASS identifies the available cellular network type (5G, 4G, LTE or H+) at the user’s current location, using an ESP32 controller paired with a SIM7600 4G/LTE modem to measure signal strength, download/upload speed and latency in real time.
Users can instantly see whether they are in a strong or weak coverage zone and pick a better nearby location for reliable connectivity, instead of guessing why their network is poor.
Combines live signal analytics (RSSI, RSRP, RSRQ, SINR) with on-device OLED display and SD-card logging in one low-cost, portable unit — a foundation for future GPS-based coverage mapping and AI-driven network analysis.
NET COMPASS

## Slide 3: TECHNICAL APPROACH
Technologies used: ESP32 DevKit (main controller), SIM7600 4G/LTE modem, 0.96” OLED display, microSD module for data logging; firmware written in C/C++ (Arduino framework) with AT-command based modem communication.
Signal flow: Cellular Network → SIM7600 Modem → ESP32 Controller → Display & Storage. Demonstration workflow: Power ON → Initialize SIM7600 → Register with Network → Acquire Parameters (RSSI/RSRP/RSRQ/SINR, speed, latency) → Display on OLED → Log to SD Card → Repeat.
NET COMPASS

## Slide 4: FEASIBILITY AND VIABILITY
Feasibility: built from off-the-shelf, low-cost components (ESP32, SIM7600, OLED, microSD) with a proven signal-flow architecture; Semester 1 budget of ₹4,000–₹7,000 keeps the prototype easily buildable and testable.
Challenges & risks: accuracy and stability of live modem readings, a deliberately limited scope (no GPS, cloud or ML in this phase), and dependency on SIM7600 network registration in low-coverage test areas.
Strategies: keep Semester 1 focused strictly on accurate, stable core data acquisition before scaling; phase GPS integration, cloud coverage mapping and AI-based analysis into Years 2 & 3 to manage complexity incrementally.
NET COMPASS

## Slide 5: IMPACT AND BENEFITS
Impact: benefits rural connectivity assessment, embedded-systems education, field engineer diagnostics and telecom network research by making invisible network quality visible and measurable at any location.
Benefits: Social — helps underserved/rural users find reliable connectivity; Economic — low-cost (₹4,000–₹7,000) alternative to expensive diagnostic equipment; Educational — hands-on embedded/telecom learning platform; scalable foundation for future coverage-mapping and AI-based services.
NET COMPASS

## Slide 6: RESEARCH AND REFERENCES
Key network parameters monitored follow standard 3GPP-defined cellular metrics: RSSI (Received Signal Strength Indicator), RSRP (Reference Signal Received Power), RSRQ (Reference Signal Received Quality) and SINR (Signal-to-Interference-plus-Noise Ratio).
Technical references: SIMCom SIM7600 series AT command manual & hardware design guide; Espressif ESP32 technical reference manual.
Prototype architecture and roadmap benchmarked against standard 4G/LTE network diagnostic practices used in field engineering and telecom research.
NET COMPASS